## Slide 1
Affordability of Screen and Treat Tools for Cervical Cancer
July 19th, 2021 – Version 1
Prepared as part of program supported by Unitaid
odemke@clintonhealthaccess.org

## Slide 2: Agenda
1 | HPV Testing | Background Existing Landscape Available global pricing & analysis On-the-ground observed costs Future efforts

## Slide 3: Current guidance from WHO has recommended HPV testing as a primary screening modality, however limitations such as pricing and infrastructure may impact scalability
Conventional PAP smear
Liquid-based cytology (LBC)
  Cytologic
  Molecular
  Visual Inspection
  Visual Inspection with Acetic Acid or with Lugol’s Iodine (VIA / VILI)
  Digital Imaging Approaches
    i.e. Automated visual evaluation (AVE)
  Nucleic Acid tests (NAT)
    HPV DNA
    mRNA
  Protein biomarkers
    HPV antibodies
    Oncoproteins
Cervical Cancer Screening

## Slide 4: Through the rapid expansion of TB and HIV testing programs, and more recently through COVID-program expansions, testing infrastructure has expanded greatly across Low-and-Middle-Income countries
Becton Dickinson (USA)
Cepheid (USA)**
Abbott Laboratories (USA)
Qiagen (USA)
Roche (Switzerland)
Hologic (USA)
>15,000 devices placed
Capable of ~20M
tests per week
ThermoFisher (USA)
MolBio (India)*
Centralized
Near Point-of-Care
Key PCR Platforms with HPV Tests
*Currently available in India, though not yet available globally
**Cepheid Omni and Edge HPV products in pipeline
Not comprehensive
Notes: ABBOTT m-2000 platforms:
~350 in Sub-Saharan Africa
CEPHEID platforms
>4000 systems deployed
ROCHE 68/8800
Hologic has ~50 Panthers
in Sub-Saharan Africa
11 countries in
Sub-Saharan Africa: installed totaling 50 platforms

## Slide 5: Pricing remains a key barrier to scale, with various key components for HPV testing driving overall pricing: test reagents and consumables, instrument, sample collection media and swabs, etc.
Total procurement
In order to run HPV NAT tests, 4 main types of commodities need to be procured from suppliers.
Products
Suppliers
  Proprietary Lab Items (Reagents and Consumables)
Test Reagents + any controls/calibrators
1
  Abbott
  Cepheid
  Hologic
  Qiagen
  Roche
  Other
Non-proprietary (generic) laboratory consumables such as:
Gloves, pipette tips, lab gowns, etc. (50+ items used per test)
*Non- specific to HPV NAT testing
  Non-Proprietary Lab Items
2
  Abbott
  LASEC
  Roche
  Other
  Sample Collection Device
3
  Proprietary
  Abbott
  Hologic
  Qiagen
  Roche
  Sample Collection Medium
Collection medium required to transport/store/prepare the sample
4
  Proprietary
  Abbott
  Qiagen
  Roche
  Other
  Non-Proprietary
  Copan
  PreservCyt
  NSS
  SurePath
  Other
  Non-Proprietary
  Aprovix AB
  Copan
  Rovers
  Other
Device for collection of cervical or vaginal specimens through either self-collection or HCW collection
Additional supplies (speculum, etc) required if HCW collection

## Slide 6: Pricing should be analyzed as a comprehensive “all-inclusive price per patient result” taking into account all costs needed to provide a patient with an actionable result
A | Reagents and consumables
B | Comprehensive service terms
C | Service bundled with cartridge
D | Instrument
E | Distribution margin
F | Delivery at place (DDP)1
G | Errors and failures
Instrument downtime Operational complexity High costs and price variability | Ensure every instrument is covered by warranty Simplifies budgeting and procurement | Incentivizes higher instrument use Simplifies budgeting & procurement | Incentivize maximum instrument use Reduce or eliminate hidden costs | Incentivize maximum instrument use Reduce or eliminate hidden costs
Components to produce a molecular diagnostic test result, grouped by price agreement
1Delivery Duty Paid (DDP) represents maximum responsibility for both costs and risk assumption from beginning to end to the seller. Seller assumes all the risks and costs of transport (export fees, carriage, insurance, and destination port charges, delivery to the final destination) and pays any import customs/duty.
Standard (default)
All components sold separately. Instrument purchased outright; separate purchasing of reagents, consumables, S&M, etc.
A
Bundled
Single price per test that includes reagents, consumables and S&M
AB
C
Reagent Rental or Placement
Instrument rented or placed; Single price includes reagents, consumables, comprehensive service terms, and the incremental cost of the instrument (if applicable); often linked to a volume commitment
Price per Patient Result (PPR)
Inclusive of all Price-per-Test components with the inclusion of errors and failures.
A
B
C
D
E
F
G
A
B
C
D
Standard
Bundled
RR / Placement
Per Patient Result
All-inclusive pricing
Price per Test (PPT)
Single price includes instrument placement, comprehensive service terms, and reagents and consumables (DDP).1 Only agreement to provide assays performed for calibration or control purposes free of charge.
A
B
C
D
E
F
Price Per Test
* Sample collection priced separately as a non-proprietary product

## Slide 7: Global pricing offers from suppliers demonstrate a diverse set of offerings
Assay | RealTime High Risk (HR) HPV |  | Aptima HPV | cobas® 4/6/8800 HPV | Xpert HPV | careHPV
Platform | m2000 sp/rt |  | Panther | 4/6/8800 | GeneXpert (IV, XVI)1 | careHPV
Manufacturer/ Developer | Abbott |  | Hologic | Roche | Cepheid | Qiagen
Test Target | HPV DNA Target Amplification |  | HPV mRNA Target Amplification | HPV DNA Target Amplification | HPV DNA Target Amplification | HPV DNA Signal Amplification
Regulatory Approval | WHO PQ |  | FDA / CE-IVD | FDA / CE-IVD (Dossier submitted to WHO PQ) | WHO PQ | WHO PQ
Per Test Pricing (Global) | $5.69 | $7.99 | $11.28 | $7.903 | $14.90 | $4.95
Price terms | Standard (reagents only) | All-inclusive | All-inclusive | Standard (reagents only) | Standard (reagents only) | Standard (reagents only)
Incoterm | FCA | DAP | DAP | CPT | Ex-works | Ex-works
Pricing Accessibility | 22 Sub-Saharan African Countries2 Other countries may be added on an ad hoc basis |  | 50 Global Access Initiative Countries | 84 Global Access Program Countries | 145 Eligible Countries | Global availability
Instrument Cost | ~$160,000 | Included in price per test | Included in price per test | cobas® 4800: ~$100,000 cobas® 6800: ~$300,000 cobas® 8800: ~$600,000 | $17,000 (Gx IV) | $10,500
Company Contacts | Francesco Marinucci, Director, Global Market Access & Funding (francesco.marinucci@abbott.com) |  | Tiffany Clarke, Director, Marketing Virology and Global Health (Tiffany.Clarke@hologic.com) | Joni Zurawinski, Sr PM, Business Development & Strategy (joni.zurawinski@roche.com) | Philippe Jacon, Senior Vice President, Global Access (Philippe.Jacon@cepheid.com) | Mark Destito Vice President, Global Health (Marc.Destito@qiagen.com)
1. Other GeneXpert models include Infinity-48 and Infinity-80. To be available soon on GeneXpert Edge
2. Angola, Benin, Burkina Faso, Burundi, Cameroon, Chad, Congo, DRC, Ethiopia, Guinea, Kenya, Liberia, Malawi, Mali, Mozambique, Nigeria, Rwanda, Senegal, South Sudan, Tanzania, Togo, Uganda.
3. This is a ceiling price associated with the volume commitment outlined above; lower prices may be accessed on a country-by-country basis
Conventional
Near Point-of-Care

## Slide 8: When accounting for additional costs including sample collection, instrument, service and maintenance, and supply chain, estimated costs increase by $1-$6
 | Abbott RealTime High Risk (HR) HPV |  | Hologic Aptima HPV | Roche cobas® 4/6/8800 HPV | Cepheid Xpert HPV | Qiagen careHPV
HPV Test (supplier price) | $5.69 | $7.99 | $11.28 | $7.90 | $14.90 | $4.95
Laboratory Costs |  |  |  |  |  | 
Reagents & proprietary consumables | ✓ | ✓ | ✓ | ✓ | ✓ | ✓
Controls | ✘ | ✓ | ✓ | ✘ | N/A | ✘
Non-proprietary consumables | ✘ | ✘ | ✘ | ✘ | ✘ | ✘
Instrument placement | ✘ | ✓ | ✓ | ✘ | ✘ | ✘
Bundled service and maintenance | ✘ | ✓ | ✓ | ✘ | ✘ | ✘
Invalid results due to instrument errors | ✘ | ✓ | ✓ | ✘ | ✘ | ✘
Supply Chain Costs (incoterms) | FCA | DAP | DAP | CPT | Ex-works | Ex-works
Pre-carriage & Export customs clearance | ✓ | ✓ | ✓ | ✓ | ✘ | ✘
Freight | ✘ | ✘ | ✓ | ✘ | ✘ | ✘
Logistics/Local Distribution | ✘ | ✘ | ✓ | ✘ | ✘ | ✘
Distributor and local agent fees | ✘ | ✘ | ✓ | ✘ | ✘ | ✘
Import duty / Taxes | ✘ | ✘ | ✘ | ✘ | ✘ | ✘
Price per Patient Test | $8.15 | $7.16 | $11.99 | $11.18 | $18.54 | $6.66
Sample Collection | $0.80 | $0.80 | $0.50 | $2.00 | $2.95 | $5.28
Total Cost | $8.95 | $7.96 | $12.49 | $13.18 | $21.49 | $11.94
Price-per-patient-test calculations include: reagents, cartridges, proprietary consumables, controls, instrument, bundled service and maintenance, grant estimates freight and insurance (10%), distributor margin (3%), and logistics/local distribution (2%). Procurement estimates from CHAI UCPOC grant PO analysis in Uganda & Tanzania and HIV VL & EID PO analysis for 2017 procurement in Uganda, Tanzania, Zimbabwe, and Malawi. Customs clearance, taxes, duties, etc assumed to be waived while supplier trainings assumed included in current pricing. Error rates from Sacks, et al 2021. Sample collection estimates include supplier specific products, where available, or a combination of PreservCyt and Rovers Cervex brush. Instrument and bundled service and maintenance costs are assumed covered by HIV/TB programs for multiplexed platforms due to existing device footprint, capacity, and program investments. Cepheid Access Care surcharge assumed covered by TB surcharge, based on structure current country SLA agreements.
Conventional
Near Point-of-Care

## Slide 9
Focused negotiations at country levels have allowed for significantly improved pricing that can be accessed by countries through setting screening targets, engagement with suppliers, and fostering competition in the market
  CHAI-Supported Countries
  Average costs paid*
Average HPV Test Cost
  $8.81 per test
  $9.82 per test
Calculated All-inclusive Cost
* Average prices paid from 2019-1H 2021 HPV test procurement through Unitaid-funded Cervical Cancer grant

## Slide 10
Support countries with developing costed screening and treatment plans, including screening targets.
Increase fundraising efforts to provide clearer projection of potential funded demand.
Increase transparency of pricing across suppliers and countries
Country-specific negotiations have achieved competitive and scalable price offerings. Can be leveraged in specific environments.
Introduction of new, affordable solutions such as through the proliferation of manual PCR platforms and validation of generic low-cost sample collection swabs and media
Further efforts will be needed to achieve a scalable target price for HPV testing
With sufficient HPV test supply, low test demand and uncertainty about HPV test uptake remains a key barrier for large-scale price reduction.
Interventions